## Slide 1
Marc Abadie, PhD
LaSIE – University of La Rochelle
mabadie@univ-lr.fr
Evaluating the Indoor Air Quality of Low-Energy Residential Buildings Session 6B
IAQ 2016 Defining Indoor Air Quality: Policy Standards and Best Practices

## Slide 2: Learning Objectives
What are the pollutants of interest in buildings?
Are there any differences between old and new (low-energy) residential buildings?
How can we evaluate/quantify the indoor air quality?

## Slide 3: Acknowledgements
Pawel Wargocki – DTU (Denmark)
Patrice Blondeau – University of La Rochelle (France)
Louis Cony – University of La Rochelle (France)
All members of IEA – Annex68

## Slide 4: Outline/Agenda
Introduction
Identification of pollutants of interest for residential buildings
Possible IAQ indices
Conclusion

## Slide 5: Indoor Air Pollutants
INFLUENCING FACTORS: Temperature, humidity, air velocity…
Identifying pollutants of interest for (low-energy) residential buildings
Providing a way to quantify the IAQ based on the selected pollutants
Inorganic
Compounds
CO, NO, NO2,
O3, SO2, NH3
…
VOC
Radon
Molds
Viruses
&
bacteria
Particules
métalliques
Pb, Cu, Se,
Cr, As, Cd
Allergens
Pollens,
mites,
...
Gaseous
Pollutants
SVOC
Pesticides, PAH,
phthalate
…
Bio-
contaminants
PM
Organic &
Mineral
Particles
Fibers
Metallic
Particles
Pb, Cu, Se,
Cr, As, Cd
GOALS

## Slide 6: Work plan
Concentration Levels in Residences
Exposure Limit Values (ELV)
Previous attempts on the
prioritization of Pollutants
Current building stock
Low energy buildings
“SHORT” LIST OF POLLUTANTS for ANNEX68
IAQ indices from literature
Based on ELV
Based on DALY
METRICS for ANNEX68
accounting for energy consumption

## Slide 7: Previous attempts on the prioritization of Pollutants
 |  |  | PM10 | PM2.5 | Nitrogen dioxide | Ozone | Sulfur dioxide | Formaldehyde | Benzene | Carbon monoxide | Naphthalene | Benzo[a]pyrene | Tetrachloroethylene | Trichloroethylene | Acrolein | Cadmium | 1,4-dichlorobenzene | Acetaldehyde | Benzo[a]anthracene | Chloroform | Fluorene | Pyrene | Furfural | Ethylbenzene | Bromoform | Styrene | Toluene | d-limonene | Chlorine | Mold | Radon | SHS | Ammonia | Crotonaldehyde | 1,1 Dichloroethene | Carbon tetrachloride | Chromium
WHO (2005) | Outdoor Air | - | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
INDEX (2005) | Indoors | Chemicals only |  |  | X |  |  | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Kirchner et al. (2006) | French Residences | - | 8 | 9 | 19 |  |  | 1 | 2 | 11 |  | 5 | 15 | 16 | 3 | 4 | 6 | 7 | 10 | 12 | 13 | 14 | 17 | 18 | 20 | 21 | 22 | 23 | 24 |  |  |  |  |  |  |  | 
WHO (2010a) | Indoor Air | Dampness/Mold |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  | 
WHO (2010b) | Indoor Air | - | X | X | X |  |  | X | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  | 
Logue et al. (2011b) | US Residences | - |  | 1 | 7 | 6 |  | 3 |  |  |  |  |  |  | 4 |  | 11 | 9 |  |  |  |  |  |  |  | 12 |  |  |  |  | 5 | 2 | 8 | 10 | 11 | 13 | 15

## Slide 8: Concentration Levels in Residences
Data from :
Kirchner et al. (2006)
Derbez et al. (2015)
Data from :
Logue et al. (2011a)
Logue et al. (2011b)

## Slide 9: Possible IAQ Indices
ELV-based approach:
  Chronic and/or Acute effects (Kirchner et al., 2006)
  Aggregation: MAX (Sharma and Bhattacharya, 2012)
PM
VOC
Bio-contami-
-nants
Radon
.
.
.
Sub-Indices
Aggregation
C1
C2
Cn
I1
I2
In
DALY-based approach:
  Chronic effects (Logue et al., 2011b)
  Acute effects (Logue et al., 2014): NO2 and CO
  Aggregation: SUM

## Slide 10: Illustrative example for France
ELV-based indices
DALY lost per year per 100,000 persons
Long-term effects / data from Kirchner et al. (2006) and Derbez et al. (2015)

## Slide 11: Conclusion
Pollutants of interest:
  List of 17 pollutants
  SVOCs have not been considered here (multiple pathways, adsorption on PM…)
Quantification of IAQ:
  Approaches:
    ELV-based approach: give a goal to designers, “to stay below the ELV level for each pollutant!”
    DALY approach: tool for decision makers, “which pollutant do we need to focus on?”
  Short/Long-term effects:
    Chronic effects = 1-2 weeks or annual average concentration
    Acute effects = 1-2 hours concentration  problem for in-situ measurements
Goal of Subtask 1: to come-up with indices to evaluate solutions for a better IAQ in low-energy residential buildings
  ELV-based approach: % of reduction of the ELV MAX with % of increase of kWhPE/m2.year
  DALY approach: % of reduction of the DALY SUM with % of increase of kWhPE/m2.year

## Slide 12: Bibliography
Derbez M, Wyart G, Douchin F, Lucas JP, Ramalho O, Ribéron J, Kirchner S, Mandin C. 2015. Base de référence nationale sur la qualité de l’air intérieur et le confort des occupants de bâtiments performants en énergie - Description des premiers résultats de la qualité de l’air intérieur et du confort de bâtiments d’habitation performants en énergie. Observatoire de la qualité de l’air intérieur, Report CSTB-OQAI/2015-012, 56 pages.
INDEX. 2005. The INDEX project: Critical Appraisal of the Setting and Implementation of Indoor exposure Limits in the EU. European Commission, Joint Research Centre, Institute for Health and Consumer Protection, Physical and Chemical Exposure Unit, Ispra, Italy (JRC/IHCP/PCE), Report, 338 pages.
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Logue JM, McKone TE, Sherman MH, Singer BC. 2011a. Hazard assessment of chemical air contaminants measured in residences. Indoor Air, 21(2), 92–109.
Logue, JM, Price PN, Sherman MH, Singer BC. 2011b. A Method to Estimate the Chronic Health Impact of Air Pollutants in U.S. Residences. Environmental Health Perspectives, 120 (2), 216–222.
Logue, JM, Sherman MH, Singer BC. 2014. A Method for Quantifying the Acute Health Impacts of Residential NonBiological Exposure Via Inhalation. LBNL Report 6883E, 11 pages.
Sharma M., Bhattacharya A. 2012. National Air Quality Index. Control of Urban Series, CUPS/82/2014-15, 58 pages.
WHO. 2005. Air quality guidelines. Global update 2005. Particulate matter, ozone, nitrogen dioxide and sulfur dioxide.
WHO. 2010a. WHO guidelines for indoor air quality: dampness and mould. World Health Organization Regional Office for Europe, Bonn, Germany.
WHO. 2010b. WHO guidelines for indoor air quality: selected pollutants. World Health Organization Regional Office for Europe, Bonn, Germany.

## Slide 13: Questions?
Marc Abadie
mabadie@univ-lr.fr