## Slide 1: Subtask 1: Defining the metrics Marc Abadie1, Pawel Wargocki2 1 LaSIE - University of La Rochelle, La Rochelle, France 2 Technical University of Denmark (DTU), Lyngby, Denmark
Indoor Air 2016 - the 14th international conference of Indoor Air Quality and Climate
Ghent, Belgium July 3-8 2016
IEA EBC Annex 68

## Slide 2: Content
2
  Introduction
  Identification of pollutants of interest for residential buildings
  IAQ indices
  Conclusion

## Slide 3: Indoor Air Pollutants
3
Identifying pollutants of interest for (low-energy) residential buildings
Providing a way to quantify the IAQ based on the selected pollutants
Inorganic
Compounds
CO, NO, NO2,
O3, SO2, NH3
…
VOC
Radon
Molds
Viruses
&
bacteria
Particules
métalliques
Pb, Cu, Se,
Cr, As, Cd
Allergens
Pollens,
mites,
...
Gaseous
Pollutants
SVOC
Pesticides, PAH,
phthalate
…
Bio-
contaminants
PM
Organic &
Mineral
Particles
Fibers
Metallic
Particles
Pb, Cu, Se,
Cr, As, Cd
INFLUENCING FACTORS: Temperature, humidity, air velocity…
GOALS
Notes: Quick presentation of pollutants of the indoor air (More than 800 compounds have been identified in indoor air)
objectives: identifying target pollutants for residential buildings AND providing a way to quantify the IAQ based on these pollutants

## Slide 4: Subtask 1 – Work plan
4
World, EU, USA, France, Belgium, Japan, China…
Concentration Levels in Residences
Exposure Limit Values (ELV)
Previous studies on the
prioritization of Pollutants
Current building stock
Low energy buildings
“SHORT” LIST OF POLLUTANTS for ANNEX68
IAQ indices from literature
Based on ELV
Based on DALY
METRICS for ANNEX68
accounting for energy consumption

## Slide 5: Identification scheme of target pollutants
5
Main steps to select the target pollutants for indoor air
STEP 1 Literature review
STEP 2 Setting-up criteria to select compounds
STEP 3 Short list
Compounds with known indoor sources and known health effects
Indoor environment: residential, commercial, office, hospital buildings
Definition of ELV / pollutant!
Compounds are excluded because:
  no expressed concerns for health at present levels
  compound already regulated by use restrictions for indoor materials
  incomplete or no dose-response data available at present levels
Annex68
Low-Energy

## Slide 6: Example: French IAQ Obs. Methodology
6
Kirchner et al. (2006):
no scientific basis for addition of health risks related to acute effects (high concentration, short time) and chronic effects (low concentration, long-time)
IAQ French campaign in dwellings (Kirchner et al., 2006): 570 houses and apartments, more than 30 parameters (chemical, biological and physical)
Acute
0
5
Chronic
0
5
Carc.
0
5
Freq.
0
5
Acute
Chronic
Carc.
Freq.
0
20
Compound | Iacute | Ichronic + Ik | Ifrequency | I
Formaldehyde | 4 | 10 | 5 | 19
Benzene | 3 | 10 | 5 | 18
Acrolein | 5 | 7 | 5 | 17
Cadmium | 1 | 10 | 5 | 16
Benzo[a]pyrene | 1 | 10 | 5 | 16
1,4-dichlorobenzene | 3 | 8 | 5 | 16
Acetaldehyde | 2 | 9 | 5 | 16
PM10 | 5 | 6 | 5 | 16
PM2.5 | 5 | 6 | 5 | 16
Benzo[a]anthracene | 1 | 9 | 5 | 15
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Notes: where
  I is the hierarchical index (0 to 20),
  Iacute and Ichronic are the indices relative to the acute and chronic health risks and range from 0 to 5 and 0 to 10, respectively.
  Ifrequency is the index relative to the presence frequency in the residential indoor air (0 to 5).
  Iacute depends on the ratio of the maximal concentration (Cmax) and the ELV for acute effects (ELVa).
  Ichronic accounts for the chronic effect potential using the mean concentration (Cmean) and the ELV for chronic effects (ELVc) and the carcinogen risk (Ik) that is equal to 0 if there is no effect and 5 if effects on human are proved.

## Slide 7: Lists of selected pollutants from previous analyses
7
WHO. 2005. Air quality guidelines. Global update 2005. Particulate matter, ozone, nitrogen dioxide and sulfur dioxide
INDEX. 2005. The INDEX project: Critical Appraisal of the Setting and Implementation of Indoor exposure Limits in the EU. European Commission, Joint Research Centre, Institute for Health and Consumer Protection, Physical and Chemical Exposure Unit, Ispra, Italy (JRC/IHCP/PCE), Report, 338 pages.
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
WHO. 2010a. WHO guidelines for indoor air quality: dampness and mould. World Health Organization Regional Office for Europe, Bonn, Germany.
WHO. 2010b. WHO guidelines for indoor air quality: selected pollutants. World Health Organization Regional Office for Europe, Bonn, Germany.
Logue, JM, Price PN, Sherman MH, Singer BC. 2011b. A Method to Estimate the Chronic Health Impact of Air Pollutants in U.S. Residences. Environmental Health Perspectives, 120 (2), 216–222.
 | WHO (2005) Outdoor Air - | INDEX (2005) Indoors Chemicals only | Kirchner et al. (2006) French Residences - | WHO (2010a) Indoor Air Dampness/Mold | WHO (2010b) Indoor Air - | Logue et al. (2011) US Residences -
PM10 | X |  | 8 |  | X | 
PM2.5 | X |  | 9 |  | X | 1
Nitrogen dioxide | X | X | 19 |  | X | 7
Ozone | X |  |  |  |  | 6
Sulfur dioxide | X |  |  |  |  | 
Formaldehyde |  | X | 1 |  | X | 3
Benzene |  | X | 2 |  | X | 
Carbon monoxide |  | X | 11 |  | X | 
Naphthalene |  | X |  |  | X | 
Benzo[a]pyrene |  |  | 5 |  | X | 
Tetrachloroethylene |  |  | 15 |  | X | 
Trichloroethylene |  |  | 16 |  | X | 
Acrolein |  |  | 3 |  |  | 4
Cadmium |  |  | 4 |  |  | 
1,4-dichlorobenzene |  |  | 6 |  |  | 11
Acetaldehyde |  |  | 7 |  |  | 9
Benzo[a]anthracene |  |  | 10 |  |  | 
Chloroform |  |  | 12 |  |  | 
Fluorene |  |  | 13 |  |  | 
Pyrene |  |  | 14 |  |  | 
Furfural |  |  | 17 |  |  | 
Ethylbenzene |  |  | 18 |  |  | 
Bromoform |  |  | 20 |  |  | 
Styrene |  |  | 21 |  |  | 12
Toluene |  |  | 22 |  |  | 
d-limonene |  |  | 23 |  |  | 
Chlorine |  |  | 24 |  |  | 
Mold |  |  |  | X |  | 
Radon |  |  |  |  | X | 5
SHS |  |  |  |  |  | 2
Ammonia |  |  |  |  |  | 8
Crotonaldehyde |  |  |  |  |  | 10
1,1 Dichloroethene |  |  |  |  |  | 11
Carbon tetrachloride |  |  |  |  |  | 13
Chromium |  |  |  |  |  | 15

## Slide 8: Indoor air pollution in low-energy residential buildings
Objective: to give an overview of people exposure to contaminants in residential buildings and to identify differences, if any, between low-energy buildings and the ones representative of the current building stock.
Mean: compiling exposure data from various countries
  mean / median concentration: long-term effects (chronic)
  maximal concentration: short-term effects (acute)
State:
8
 |  | France | USA | Belgium | China | Japan
Current building stock | Cmean | Kirchner et al. (2006) | Logue et al. (2010) | Stranger et al. (2012) | Zhang et al. (2013) | Azuma et al. (2007)
 | Cmax | Kirchner et al. (2006) |  | Stranger et al. (2012) |  | Azuma et al. (2007)
Low-energy buidings | Cmean | Derbez et al. (2015) | Logue et al. (2010) | Stranger et al. (2012) | Liang et al. (2014) | 
 | Cmax | Derbez et al. (2015) |  | Stranger et al. (2012) |  | 
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Derbez M, Wyart G, Douchin F, Lucas JP, Ramalho O, Ribéron J, Kirchner S, Mandin C. 2015. Base de référence nationale sur la qualité de l’air intérieur et le confort des occupants de bâtiments performants en énergie - Description des premiers résultats de la qualité de l’air intérieur et du confort de bâtiments d’habitation performants en énergie. Observatoire de la qualité de l’air intérieur, Report CSTB-OQAI/2015-012, 56 pages.
Logue JM, McKone TE, Sherman MH, Singer BC. 2011a. Hazard assessment of chemical air contaminants measured in residences. Indoor Air, 21(2), 92–109.
Stranger et al. 2012. Clean Air, Low Energy Exploratory research on the quality of the indoor environment in energy‐efficient buildings: the influence of outdoor environment and ventilation, report, 346p., November.
Zhang et al. 2013. Reducing Health Risks from Indoor Exposures in Rapidly Developing Urban China, Environmental Health Perspectives; 121 (7), pp. 751-755.
Liang, Weihui, Caiqing Yang, and Xudong Yang. 2014. Long-Term Concentrations of Volatile Organic Compounds in a New Apartment in Beijing, China. Building and Environment, 82, pp. 693–701.
Azuma et al. 2007. The Risk Screening for Indoor Air Pollution Chemicals in Japan, Risk Analysis, 27 (6), pp.

## Slide 9: Indoor air pollution in low-energy residential buildings
Objective: to give an overview of people exposure to contaminants in residential buildings and to identify differences, if any, between low-energy buildings and the ones representative of the current building stock.
Mean: compiling exposure data from various countries
  mean / median concentration: long-term effects (chronic)
  maximal concentration: short-term effects (acute)
State:
9
 |  | France | USA | Belgium | China | Japan
Current building stock | Cmean | Kirchner et al. (2006) | Logue et al. (2010) | Stranger et al. (2012) | Zhang et al. (2013) | Azuma et al. (2007)
 | Cmax | Kirchner et al. (2006) |  | Stranger et al. (2012) |  | Azuma et al. (2007)
Low-energy buidings | Cmean | Derbez et al. (2015) | Logue et al. (2010) | Stranger et al. (2012) | Liang et al. (2014) | 
 | Cmax | Derbez et al. (2015) |  | Stranger et al. (2012) |  | 
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Derbez M, Wyart G, Douchin F, Lucas JP, Ramalho O, Ribéron J, Kirchner S, Mandin C. 2015. Base de référence nationale sur la qualité de l’air intérieur et le confort des occupants de bâtiments performants en énergie - Description des premiers résultats de la qualité de l’air intérieur et du confort de bâtiments d’habitation performants en énergie. Observatoire de la qualité de l’air intérieur, Report CSTB-OQAI/2015-012, 56 pages.
Logue JM, McKone TE, Sherman MH, Singer BC. 2011a. Hazard assessment of chemical air contaminants measured in residences. Indoor Air, 21(2), 92–109.
Stranger et al. 2012. Clean Air, Low Energy Exploratory research on the quality of the indoor environment in energy‐efficient buildings: the influence of outdoor environment and ventilation, report, 346p., November.
Zhang et al. 2013. Reducing Health Risks from Indoor Exposures in Rapidly Developing Urban China, Environmental Health Perspectives; 121 (7), pp. 751-755.
Liang, Weihui, Caiqing Yang, and Xudong Yang. 2014. Long-Term Concentrations of Volatile Organic Compounds in a New Apartment in Beijing, China. Building and Environment, 82, pp. 693–701.
Azuma et al. 2007. The Risk Screening for Indoor Air Pollution Chemicals in Japan, Risk Analysis, 27 (6), pp.
Q2: Do you know any national campaigns for the evaluation of pollutant concentration levels in residential buildings other than the ones presented during the workshop?

## Slide 10: Indoor air pollution in low-energy residential buildings
10
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Derbez M, Wyart G, Douchin F, Lucas JP, Ramalho O, Ribéron J, Kirchner S, Mandin C. 2015. Base de référence nationale sur la qualité de l’air intérieur et le confort des occupants de bâtiments performants en énergie - Description des premiers résultats de la qualité de l’air intérieur et du confort de bâtiments d’habitation performants en énergie. Observatoire de la qualité de l’air intérieur, Report CSTB-OQAI/2015-012, 56 pages.

## Slide 11: Indoor air pollution in low-energy residential buildings
11
Logue JM, McKone TE, Sherman MH, Singer BC. 2011a. Hazard assessment of chemical air contaminants measured in residences. Indoor Air, 21(2), 92–109.

## Slide 12: Exposure Limit Values (ELV)
12
Objective: to define the ELV to be used in the current project.
Mean: compiling the Indoor Air Guideline Values (IAGV) from various countries (World, EU, France, Belgium, Germany, China, Hong-Kong, Canada, California…)

## Slide 13: Exposure Limit Values (ELV) Long-term exposure
13

## Slide 14: Exposure Limit Values (ELV) Long-term exposure
14
Q3: Do you know any national Indoor Air Guidelines other than the ones presented during the workshop?

## Slide 15: ANNEX 68 – Short list of pollutants of interest
15
 | ELV for long-term exposure | ELV for short-term exposure
PM2.5 | X | X
Radon | X | 
Ozone | X (WHO for Outdoor Air) | X
Formaldehyde | X | X
Acrolein | X | X
Mold | X | 
Nitrogen dioxide | X | X
Benzene | X | X
Styrene | X | X
Toluene | X | X
Hexanal | X (LCI) | 
alpha-Pinene | X | 
Naphthalene | X | 
Trichloroethylene | X | X
Tetrachloroethylene | X | X
1,4-dichlorobenzene | X | 
Xylene | X | X

## Slide 16: ANNEX 68 – Short list of pollutants of interest
16
 | ELV for long-term exposure | ELV for short-term exposure
PM2.5 | X | X
Radon | X | 
Ozone | X (WHO for Outdoor Air) | X
Formaldehyde | X | X
Acrolein | X | X
Mold | X | 
Nitrogen dioxide | X | X
Benzene | X | X
Styrene | X | X
Toluene | X | X
Hexanal | X (LCI) | 
alpha-Pinene | X | 
Naphthalene | X | 
Trichloroethylene | X | X
Tetrachloroethylene | X | X
1,4-dichlorobenzene | X | 
Xylene | X | X
Q X: Do we miss something?
Can we delete some from this list?...

## Slide 17: IAQ indices: the problematic
17
Step 1: Sub-indices
Sharma M., Bhattacharya A, 2012, National Air Quality Index. Control of Urban Series, CUPS/82/2014-15, 58 pages.
PM
VOC
Bio-contami--nants
Radon
.
.
.
Sub-Indices
Aggregation
 | Grade for PM10 (µg/m3, 24h) - Chiang and Lai (2002) |  |  |  |  |  |  |  | 
Grade | 20 |  | 40 |  | 60 |  | 80 |  | 100
Ci |  | >350 | X | >150 |  | >50 |  | >25 | 
adapted from IND-QAI (Sharma and Bhattacharya, 2012)
Notes: The first part was to define our set of pollutants of interest by analyzing previous studies and data. Now, we are looking to the future… how to evaluate the IAQ from measurement or modelling…

## Slide 18: IAQ indices: the problematic
18
Step 2: Aggregation of Sub-indices
  Weighted Additive Form
  Root-Sum-Power Form (non-linear aggregation form)
  Root-Mean-Square Form
  Max Operator
PM
VOC
Bio-contami--nants
Radon
.
.
.
Sub-Indices
Aggregation

## Slide 19: IAQ indices: the problematic
Aggregation limitations (Sharma and Bhattacharya, 2012):
19
Non-ambiguous and non-eclipsing aggregation = Max (sub-indices)
Sharma M., Bhattacharya A, 2012, National Air Quality Index. Control of Urban Series, CUPS/82/2014-15, 58 pages.
0
2
0
2
1
1
Ambiguity
0
2
0
2
1
1
Eclipsing

## Slide 20: IAQ indices from literature (based on Kirchner, Jédor and Mandin, 2006)
Gadeau (1996)
CO, CO2, NO2, HCHO
Castanet (1998)
CO, CO2, Bacteria
Chiang and Lai (2002)
CO, CO2, HCHO, TVOC, PM10
QUAD-BBC (2012)
CO2, NO2, SO2, O3, CO, HCHO, Acetaldehyde, Ethylbenzene,
Styrene, Toluene, o-Xylene, Acetone, PM2.5, PM10
Sofuoglu and Moschandreas (2003)
Formaldehyde, TVOC, CO, CO2, PM2.5, PM10, Fungi, Bacteria
20
Max. operator
Cohas (1996)
any pollutant
Weighted Additive Form
Kirchner S, Jédor B, Mandin C. 2006. Elaboration d’indices de la qualité de l’air intérieur : phase 1 – Inventaire des indices disponibles. Report DDD-SB/2006-065, 49 pages.

## Slide 21: IAQ indices from literature (based on Kirchner, Jédor and Mandin, 2006)
Gadeau (1996)
CO, CO2, NO2, HCHO
Castanet (1998)
CO, CO2, Bacteria
Chiang and Lai (2002)
CO, CO2, HCHO, TVOC, PM10
QUAD-BBC (2012)
CO2, NO2, SO2, O3, CO, HCHO, Acetaldehyde, Ethylbenzene,
Styrene, Toluene, o-Xylene, Acetone, PM2.5, PM10
Sofuoglu and Moschandreas (2003)
Formaldehyde, TVOC, CO, CO2, PM2.5, PM10, Fungi, Bacteria
21
Max. operator
Cohas (1996)
any pollutant
Weighted Additive Form
Kirchner S, Jédor B, Mandin C. 2006. Elaboration d’indices de la qualité de l’air intérieur : phase 1 – Inventaire des indices disponibles. Report DDD-SB/2006-065, 49 pages.
Q4: Do you know any Indoor Air Indices other than the ones presented during the workshop?

## Slide 22: The DALY approach (Logue et al., 2011)
22
Disability-Adjusted Life-Years (DALY):
Logue, JM, Price PN, Sherman MH, Singer BC. 2011b. A Method to Estimate the Chronic Health Impact of Air Pollutants in U.S. Residences. Environmental Health Perspectives, 120 (2), 216–222.
YLLdisease : Years of Life Lost due to premature death from the disease,
YLDdisease: Years of Life Disability, weighted from 0 to 1 depending on disease severity.
2 methods according to initial data:
Intake-Incidence-DALY method:
  Epidemiology based concentration-response (CR) functions to quantify disease incidence rates + estimates of DALYs per disease incidence reported in the literature.
: number of persons exposed (usually 100,000),
: baseline prevalence of illness per year,
: coefficient of the concentration change (natural logarithm of the relative risk divided by the change in mean/median exposure),
exposure-related concentration (µg/m3).

## Slide 23: The DALY approach
23
Principle (Logue et al., 2011):
Logue, JM, Price PN, Sherman MH, Singer BC. 2011b. A Method to Estimate the Chronic Health Impact of Air Pollutants in U.S. Residences. Environmental Health Perspectives, 120 (2), 216–222.
Huilbregts Mark A.J , Rombouts Linda J.A, Ragas M.J, and van de Meen Dik, “Human-Toxicological Effect and Damage Factors of Carcinogenic and Noncarinogenic Chemicals for Life Cycle Assessment.” Integrated Environmental Assessment and Management Volume 1, no.3 (February 2005): 181-244.
YLLdisease : Years of Life Lost due to premature death from the disease,
YLDdisease: Years of Life Disability, weighted from 0 to 1 depending on disease severity.
2 methods according to initial data:
Intake-DALY approach:
  Used the work of Huijbregts et al. (2005) to calculate the health impact associated with intake of pollutants based on animal toxicity literature.
: Age-Dependent Adjustment Factor (-),
: volume rate of air intake (m3/day),
: considered period of time (day, usually 365),
exposure-related concentration (µg/m3).

## Slide 24: ELV-based or DALY approaches
Illustrative example:
  Concentration levels in residences in France
    Data for current building stock: Kirchner et al (2006)
    Data for low-energy buildings: Derbez et al. (2015)
  Selected pollutants from our list of 17 pollutants
    Available concentration levels for both cases (note: acrolein level was not available in Derbez et al. (2015))
    Available ELV and DALY parameters for chronic effects
    When several ELV were available for one pollutant, the minimal value has been chosen
24
Benzene, Formaldehyde, Nitrogen Dioxide, PM2.5,
Styrene, Tetrachloroethylene, Toluene and Trichloroethylene.

## Slide 25: ELV-based or DALY approaches
25
ELV-based indices
DALY lost per year per 100,000 persons
Formaldehyde, PM2.5
Nitrogen Dioxide, Benzene
PM2.5, Formaldehyde
Notes: Different conclusions

## Slide 26: ELV-based or DALY approaches
26
 | Current building stock | Low Energy buildings
Benzene | 0.01 | 0.01
Formaldehyde | 9.85 | 8.90
Nitrogen dioxide | 2.15 | 0.91
PM2.5 | 1242.22 | 1157.09
Styrene | 0.02 | 0.68
Tetrachloroethylene | 0.02 | 0.01
Toluene | 0.01 | 0.01
Trichloroethylene | 0.00 | 0.00
Sum | 1254.29 | 1167.60
 |  | -7%
ELV-based indices
DALY lost per year per 100,000 persons
 | Current building stock | Low Energy buildings
Benzene | 1.05 | 0.85
Formaldehyde | 2.18 | 1.97
Nitrogen dioxide | 1.63 | 0.67
PM2.5 | 1.91 | 1.74
Styrene | 0.03 | 0.04
Tetrachloroethylene | 0.01 | 0.00
Toluene | 0.05 | 0.02
Trichloroethylene | 0.05 | 0.05
Max | 2.18 | 1.97
 |  | -10%

## Slide 27: Conclusions
Pollutants of interest:
  List of 17 pollutants (that could probably be shortened)
  SVOCs have not been considered here
Quantification of IAQ:
  ELV-based approach: give a goal to designers, “to stay below the ELV level for each pollutant!”
  DALY approach: tool for decision makers, “which pollutant do we need to focus on?”
Goal of Subtask 1: to come-up with indices to evaluate solutions for a better IAQ in low-energy residential buildings
  ELV-based approach: % of reduction of the max (or each pollutant index) with % of increase of kWhPE/m2.year
  DALY approach: % of reduction of the total DALY with % of increase of kWhPE/m2.year
27