## Slide 1: Subtask 1: Defining the metrics Marc Abadie1, Pawel Wargocki2 1 LaSIE - University of La Rochelle, La Rochelle, France 2 Technical University of Denmark (DTU), Lyngby, Denmark
The 2nd Expert Meeting of the International Energy Agency Annex 68 Project Indoor Air Quality Design and Control in Low Energy Residential Buildings
September 8-10, 2016
IEA EBC Annex 68

## Slide 2: Content
2
  Introduction
  Identification of pollutants of interest for residential buildings
  IAQ indices
  Conclusion

## Slide 3: Indoor Air Pollutants
3
Identifying pollutants of interest for (low-energy) residential buildings
Providing a way to quantify the IAQ based on the selected pollutants
Inorganic
Compounds
CO, NO, NO2,
O3, SO2, NH3
…
VOC
Radon
Molds
Viruses
&
bacteria
Particules
métalliques
Pb, Cu, Se,
Cr, As, Cd
Allergens
Pollens,
mites,
...
Gaseous
Pollutants
SVOC
Pesticides, PAH,
phthalate
…
Bio-
contaminants
PM
Organic &
Mineral
Particles
Fibers
Metallic
Particles
Pb, Cu, Se,
Cr, As, Cd
INFLUENCING FACTORS: Temperature, humidity, air velocity…
GOALS
Notes: Quick presentation of pollutants of the indoor air (More than 800 compounds have been identified in indoor air)
objectives: identifying target pollutants for residential buildings AND providing a way to quantify the IAQ based on these pollutants

## Slide 4: Subtask 1 – Work plan
4
World, EU, USA, France, Belgium, Japan, China…
Concentration Levels in Residences
Exposure Limit Values (ELV)
Previous studies on the
prioritization of Pollutants
Current building stock
Low energy buildings
“SHORT” LIST OF POLLUTANTS for ANNEX68
IAQ indices from literature
Based on ELV
Based on DALY
METRICS for ANNEX68
accounting for energy consumption

## Slide 5: Identification scheme of target pollutants
5
Main steps to select the target pollutants for indoor air
STEP 1 Literature review
STEP 2 Setting-up criteria to select compounds
STEP 3 Short list
Compounds with known indoor sources and known health effects
Indoor environment: residential, commercial, office, hospital buildings
Definition of ELV / pollutant!
Compounds are excluded because:
  no expressed concerns for health at present levels
  compound already regulated by use restrictions for indoor materials
  incomplete or no dose-response data available at present levels
Annex68
Low-Energy

## Slide 6: Lists of selected pollutants from previous analyses
6
WHO. 2005. Air quality guidelines. Global update 2005. Particulate matter, ozone, nitrogen dioxide and sulfur dioxide
INDEX. 2005. The INDEX project: Critical Appraisal of the Setting and Implementation of Indoor exposure Limits in the EU. European Commission, Joint Research Centre, Institute for Health and Consumer Protection, Physical and Chemical Exposure Unit, Ispra, Italy (JRC/IHCP/PCE), Report, 338 pages.
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
WHO. 2010a. WHO guidelines for indoor air quality: dampness and mould. World Health Organization Regional Office for Europe, Bonn, Germany.
WHO. 2010b. WHO guidelines for indoor air quality: selected pollutants. World Health Organization Regional Office for Europe, Bonn, Germany.
Logue, JM, Price PN, Sherman MH, Singer BC. 2011b. A Method to Estimate the Chronic Health Impact of Air Pollutants in U.S. Residences. Environmental Health Perspectives, 120 (2), 216–222.
 | WHO (2005) Outdoor Air - | INDEX (2005) Indoors Chemicals only | Kirchner et al. (2006) French Residences - | WHO (2010a) Indoor Air Dampness/Mold | WHO (2010b) Indoor Air - | Logue et al. (2011) US Residences -
PM10 | X |  | 8 |  | X | 
PM2.5 | X |  | 9 |  | X | 1
Nitrogen dioxide | X | X | 19 |  | X | 7
Ozone | X |  |  |  |  | 6
Sulfur dioxide | X |  |  |  |  | 
Formaldehyde |  | X | 1 |  | X | 3
Benzene |  | X | 2 |  | X | 
Carbon monoxide |  | X | 11 |  | X | 
Naphthalene |  | X |  |  | X | 
Benzo[a]pyrene |  |  | 5 |  | X | 
Tetrachloroethylene |  |  | 15 |  | X | 
Trichloroethylene |  |  | 16 |  | X | 
Acrolein |  |  | 3 |  |  | 4
Cadmium |  |  | 4 |  |  | 
1,4-dichlorobenzene |  |  | 6 |  |  | 11
Acetaldehyde |  |  | 7 |  |  | 9
Benzo[a]anthracene |  |  | 10 |  |  | 
Chloroform |  |  | 12 |  |  | 
Fluorene |  |  | 13 |  |  | 
Pyrene |  |  | 14 |  |  | 
Furfural |  |  | 17 |  |  | 
Ethylbenzene |  |  | 18 |  |  | 
Bromoform |  |  | 20 |  |  | 
Styrene |  |  | 21 |  |  | 12
Toluene |  |  | 22 |  |  | 
d-limonene |  |  | 23 |  |  | 
Chlorine |  |  | 24 |  |  | 
Mold |  |  |  | X |  | 
Radon |  |  |  |  | X | 5
SHS |  |  |  |  |  | 2
Ammonia |  |  |  |  |  | 8
Crotonaldehyde |  |  |  |  |  | 10
1,1 Dichloroethene |  |  |  |  |  | 11
Carbon tetrachloride |  |  |  |  |  | 13
Chromium |  |  |  |  |  | 15

## Slide 7: Indoor air pollution in low-energy residential buildings
Objective: to give an overview of people exposure to contaminants in residential buildings and to identify differences, if any, between low-energy buildings and the ones representative of the current building stock.
Mean: compiling exposure data from various countries
  mean / median concentration: long-term effects (chronic)
  maximal concentration: short-term effects (acute)
State:
7
 |  | France | USA | Belgium | China | Japan
Current building stock | Cmean | Kirchner et al. (2006) | Logue et al. (2010) | Stranger et al. (2012) | Zhang et al. (2013) | Azuma et al. (2007)
 | Cmax | Kirchner et al. (2006) |  | Stranger et al. (2012) |  | Azuma et al. (2007)
Low-energy buidings | Cmean | Derbez et al. (2015) | Logue et al. (2010) | Stranger et al. (2012) | Liang et al. (2014) | 
 | Cmax | Derbez et al. (2015) |  | Stranger et al. (2012) |  | 
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Derbez M, Wyart G, Douchin F, Lucas JP, Ramalho O, Ribéron J, Kirchner S, Mandin C. 2015. Base de référence nationale sur la qualité de l’air intérieur et le confort des occupants de bâtiments performants en énergie - Description des premiers résultats de la qualité de l’air intérieur et du confort de bâtiments d’habitation performants en énergie. Observatoire de la qualité de l’air intérieur, Report CSTB-OQAI/2015-012, 56 pages.
Logue JM, McKone TE, Sherman MH, Singer BC. 2011a. Hazard assessment of chemical air contaminants measured in residences. Indoor Air, 21(2), 92–109.
Stranger et al. 2012. Clean Air, Low Energy Exploratory research on the quality of the indoor environment in energy‐efficient buildings: the influence of outdoor environment and ventilation, report, 346p., November.
Zhang et al. 2013. Reducing Health Risks from Indoor Exposures in Rapidly Developing Urban China, Environmental Health Perspectives; 121 (7), pp. 751-755.
Liang, Weihui, Caiqing Yang, and Xudong Yang. 2014. Long-Term Concentrations of Volatile Organic Compounds in a New Apartment in Beijing, China. Building and Environment, 82, pp. 693–701.
Azuma et al. 2007. The Risk Screening for Indoor Air Pollution Chemicals in Japan, Risk Analysis, 27 (6), pp.

## Slide 8: Indoor air pollution in low-energy residential buildings
8
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Derbez M, Wyart G, Douchin F, Lucas JP, Ramalho O, Ribéron J, Kirchner S, Mandin C. 2015. Base de référence nationale sur la qualité de l’air intérieur et le confort des occupants de bâtiments performants en énergie - Description des premiers résultats de la qualité de l’air intérieur et du confort de bâtiments d’habitation performants en énergie. Observatoire de la qualité de l’air intérieur, Report CSTB-OQAI/2015-012, 56 pages.

## Slide 9: Indoor air pollution in low-energy residential buildings
9
Logue JM, McKone TE, Sherman MH, Singer BC. 2011a. Hazard assessment of chemical air contaminants measured in residences. Indoor Air, 21(2), 92–109.

## Slide 10: Exposure Limit Values (ELV)
10
Objective: to define the ELV to be used in the current project.
Mean: compiling the Indoor Air Guideline Values (IAGV) from various countries (World, EU, France, Belgium, Germany, China, Hong-Kong, Canada, California…)

## Slide 11: Exposure Limit Values (ELV) Long-term exposure
11

## Slide 12: ANNEX 68 – Short list of pollutants of interest
12
 | ELV for long-term exposure | ELV for short-term exposure
PM2.5 | X | X
Radon | X | 
Ozone | X (WHO for Outdoor Air) | X
Formaldehyde | X | X
Acrolein | X | X
Mold | X | 
Nitrogen dioxide | X | X
Benzene | X | X
Styrene | X | X
Toluene | X | X
Hexanal | X (LCI) | 
alpha-Pinene | X | 
Naphthalene | X | 
Trichloroethylene | X | X
Tetrachloroethylene | X | X
1,4-dichlorobenzene | X | 
Xylene | X | X

## Slide 13: IAQ indices: the problematic
13
Sharma M., Bhattacharya A, 2012, National Air Quality Index. Control of Urban Series, CUPS/82/2014-15, 58 pages.
Kirchner S, Arene JF, Cochet C, Derbez M, Duboudin C, Elias P, Gregoire A, Jedor B, Lucas JP, Pasquier N, Pigneret M, Ramalho O. 2006. Campagne nationale logements: état de la pollution dans les logements français. Report, CSTB/DDD/SB – 2006-57, 165 pages.
Logue, JM, Price PN, Sherman MH, Singer BC. 2011b. A Method to Estimate the Chronic Health Impact of Air Pollutants in U.S. Residences. Environmental Health Perspectives, 120 (2), 216–222.
Logue, JM, Sherman MH, Singer BC. 2014. A Method for Quantifying the Acute Health Impacts of Residential NonBiological Exposure Via Inhalation. LBNL Report 6883E, 11 pages.
PM
VOC
Bio-contami--nants
Radon
.
.
.
Sub-Indices
Aggregation
adapted from IND-QAI (Sharma and Bhattacharya, 2012)
ELV-based approach:
  Chronic and/or Acute effects (Kirchner et al., 2006)
  Aggregation: MAX (Sharma and Bhattacharya, 2012)
DALY-based approach:
  Chronic effects (Logue et al., 2011b)
  Acute effects (Logue et al., 2014): NO2 and CO
  Aggregation: SUM
Notes: The first part was to define our set of pollutants of interest by analyzing previous studies and data. Now, we are looking to the future… how to evaluate the IAQ from measurement or modelling…

## Slide 14: ELV-based or DALY approaches
14
ELV-based indices
DALY lost per year per 100,000 persons
Formaldehyde, PM2.5
Nitrogen Dioxide, Benzene
PM2.5, Formaldehyde
Long-term effects / data from Kirchner et al. (2006) and Derbez et al. (2015)
Wrong value
Notes: Different conclusions

## Slide 15: ELV-based or DALY approaches
15
Long-term effects / data from Kirchner et al. (2006) and Derbez et al. (2015)
ELV-based indices
DALY lost per year per 100,000 persons
Wrong value

## Slide 16: Conclusions
Pollutants of interest:
  List of 17 pollutants
  SVOCs have not been considered here (multiple pathways, adsorption on PM…)
Quantification of IAQ:
  Approaches:
    ELV-based approach: give a goal to designers, “to stay below the ELV level for each pollutant!”
    DALY approach: tool for decision makers, “which pollutant do we need to focus on?”
  Short/Long-term effects:
    Chronic effects = 1-2 weeks or annual average concentration
    Acute effects = 1-2 hours concentration  problem for in-situ measurements
Goal of Subtask 1: to come-up with indices to evaluate solutions for a better IAQ in low-energy residential buildings
  ELV-based approach: % of reduction of the ELV MAX with % of increase of kWhPE/m2.year
  DALY approach: % of reduction of the DALY SUM with % of increase of kWhPE/m2.year
16